Ospf net working :
ospf stands for open sortest path first

setting up:

there is three router each router connected with the two pc with a switch and the each of the router connected with a serial cable

enough talk lest start configuring :) :) :)

first router:
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#do show ip interface brief

Router(config)#interface GigabitEthernet0/0
Router(config-if)#ip address 192.168.0.1 255.255.255.0
Router(config-if)#no shutdown

Router(config-if)#
Router(config-if)#exit
Router(config)#interface Serial0/3/0
Router(config-if)#ip address 10.0.0.1 255.0.0.0
Router(config-if)#no shutdown

router 2:
Router>
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#do show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 unassigned YES unset administratively down down
GigabitEthernet0/1 unassigned YES unset administratively down down
GigabitEthernet0/2 unassigned YES unset administratively down down
Serial0/3/0 unassigned YES unset administratively down down
Serial0/3/1 unassigned YES unset administratively down down
Vlan1 unassigned YES unset administratively down down
Router(config)#interface GigabitEthernet0/0
Router(config-if)#ip address 192.168.1.1 255.255.255.0
Router(config-if)#no shutdown

Router(config-if)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0, changed state to up

Router(config-if)#exit
Router(config)#interface Serial0/3/0
Router(config-if)#ip address 10.0.0.2 255.0.0.0
Router(config-if)#no shutdown

Router(config-if)#
%LINK-5-CHANGED: Interface Serial0/3/0, changed state to up

Router(config-if)#exit
Router(config)#in
%LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/3/0, changed state to u
Router(config)#interface Serial0/3/1
Router(config-if)#ip address 11.0.0.1 255.0.0.0
Router(config-if)#no shutdown

%LINK-5-CHANGED: Interface Serial0/3/1, changed state to down
Router(config-if)#
Router(config-if)#exit
Router(config)#^Z
Router#
%SYS-5-CONFIG_I: Configured from console by console

Router#

router3:
Router>enable
Router#configure
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#do show ip interface brief
Interface IP-Address OK? Method Status Protocol
GigabitEthernet0/0 unassigned YES unset administratively down down
GigabitEthernet0/1 unassigned YES unset administratively down down
GigabitEthernet0/2 unassigned YES unset administratively down down
Serial0/3/0 unassigned YES unset administratively down down
Serial0/3/1 unassigned YES unset administratively down down
Vlan1 unassigned YES unset administratively down down
Router(config)#interface GigabitEthernet0/0
Router(config-if)#ip address 192.168.2.1 255.255.255.0
Router(config-if)#no shut

Router(config-if)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0, changed state to up

Router(config-if)#exit
Router(config)#interface Serial0/3/1
Router(config-if)#ip address 11.0.0.2 255.0.0.0
Router(config-if)#no shutdown

Router(config-if)#
%LINK-5-CHANGED: Interface Serial0/3/1, changed state to up

Router(config-if)#
Router(config-if)#
%LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/3/1, changed state to up

Router(config-if)#

its ospf time:
remember one thing we use wildcard insted of the subnet mask
its the oppsite of the subnet mask
subnetmask = 255.255.0.0
then the wildcardbit: 0. 0.255.255

its just like the eigrp but all you have to do is add a area <number> just like that

remember process id can be different but area shoud be same for this configuration

go to the router1:
Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router ospf ?
<1-65535> Process ID
Router(config)#router ospf 100
Router(config-router)#network 192.168.0.0 0.0.0.255 area 0
Router(config-router)#network 10.0.0.0 255.255.255.0 area 0
Router(config-router)#

go to router 2: there is three network we have to add it:

Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router ospf 120
Router(config-router)#network 10.0.0.0 0.255.255.255 area 0
00:20:17: %OSPF-5-ADJCHG: Process 120, Nbr 192.168.0.1 on Serial0/3/0 from LOADING to FULL, Loading Done
Router(config-router)#network 192.168.1.0 0.255.255.255 area 0
Router(config-router)#network 11.0.0.0 0.255.255.255 area 0
Router(config-router)#

router3:

Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#router ospf 130
Router(config-router)#network 11.0.0.0 0.255.255.255 area 0
Router(config-router)#
00:25:15: %OSPF-5-ADJCHG: Process 130, Nbr 11.0.0.1 on Serial0/3/1 from LOADING to FULL, Loading Done

Router(config-router)#network 192.168.2.00.0.0.255 area 0

Router(config-router)#network 192.168.2.0 0.0.0.255 area 0
Router(config-router)#

done this is the same area network ospf can do different network