Switch>enable

Switch#configure terminal

Switch(config)#do show vlan
result

VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Fa0/1, Fa0/2, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gig0/1, Gig0/2
1002 fddi-default act/unsup
1003 token-ring-default act/unsup
1004 fddinet-default act/unsup
1005 trnet-default act/unsup

VLAN Type SAID MTU Parent RingNo BridgeNo Stp BrdgMode Trans1 Trans2
---- ----- ---------- ----- ------ ------ -------- ---- -------- ------ ------
1 enet 100001 1500 - - - - - 0 0
1002 fddi 101002 1500 - - - - - 0 0
1003 tr 101003 1500 - - - - - 0 0
1004 fdnet 101004 1500 - - - ieee - 0 0
1005 trnet 101005 1500 - - - ibm - 0 0
adding vlan
Switch(config)#vlan 2
Switch(config-vlan)#name sales //give the name
.
 Switch(config)#vlan 3
Switch(config-vlan)#name eng
Switch(config-vlan)#exit
Switch(config)#vlan 4
Switch(config-vlan)#name manage
Switch(config-vlan)#exit
Switch(config)#do show vlan

vlan create complete now asssign the port to vlan remember vlan works with the port not any ip

Switch#enable
Switch#configure terminal

**************adding two port to the vlan 2*****************
Switch(config)#interface fastEthernet 0/1

Switch(config-if)#switchport access vlan 2
Switch(config-if)#exit

Switch(config)#interface fastEthernet 0/2

Switch(config-if)#switchport access vlan 2

Switch(config-if)#exit

**************adding two port to the vlan 3*****************

Switch(config)#interface fastEthernet 0/3

Switch(config-if)#switchport access vlan 3
Switch(config-if)#exit

Switch(config)#interface fastEthernet 0/4

Switch(config-if)#switchport access vlan 3
Switch(config-if)#exit

Switch(config)#interface fastEthernet 0/5

**************adding two port to the vlan 4 *****************

Switch(config-if)#switchport access vlan 4
Switch(config-if)#exit

Switch(config)#interface fastEthernet 0/6

Switch(config-if)#switchport access vlan 4
Switch(config-if)#exit

now if we ping from a device from onw vlan to anotherr vlan we can ping it.becaue the broadcast domain has been divided and one vlan pc cant talk to another vlan pc

what is dot 1 q encapsulation??

 dot 1 q encapsulation acctually change the datalink frame header and add the vlan information and add traler to for the confimation switch can understand which vlan it has to send