Virtual trunking protocols:

switch:

Switch>
Switch>
Switch>enable
Switch#config terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#do sh vlan

VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Fa0/1, Fa0/2, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gig0/1, Gig0/2
1002 fddi-default active
1003 token-ring-default active
1004 fddinet-default active
1005 trnet-default active

VLAN Type SAID MTU Parent RingNo BridgeNo Stp BrdgMode Trans1 Trans2
---- ----- ---------- ----- ------ ------ -------- ---- -------- ------ ------
1 enet 100001 1500 - - - - - 0 0
1002 fddi 101002 1500 - - - - - 0 0
1003 tr 101003 1500 - - - - - 0 0
1004 fdnet 101004 1500 - - - ieee - 0 0
1005 trnet 101005 1500 - - - ibm - 0 0

Switch(config)#vlan 10
Switch(config-vlan)#name yellow
Switch(config-vlan)#exit
Switch(config)#vlan 20
Switch(config-vlan)#name green'
Switch(config-vlan)#n0 name green'
^
% Invalid input detected at '^' marker.
Switch(config-vlan)#no name green'
Switch(config-vlan)#name green
Switch(config-vlan)#exit
Switch(config)#vlan 30
Switch(config-vlan)#name blue
Switch(config-vlan)#exit
Switch(config)#do sh vlan

VLAN Name Status Ports
---- -------------------------------- --------- -------------------------------
1 default active Fa0/1, Fa0/2, Fa0/3, Fa0/4
Fa0/5, Fa0/6, Fa0/7, Fa0/8
Fa0/9, Fa0/10, Fa0/11, Fa0/12
Fa0/13, Fa0/14, Fa0/15, Fa0/16
Fa0/17, Fa0/18, Fa0/19, Fa0/20
Fa0/21, Fa0/22, Fa0/23, Fa0/24
Gig0/1, Gig0/2
10 yellow active
20 green active
30 blue active
1002 fddi-default active
1003 token-ring-default active
1004 fddinet-default active
1005 trnet-default active

VLAN Type SAID MTU Parent RingNo BridgeNo Stp BrdgMode Trans1 Trans2
---- ----- ---------- ----- ------ ------ -------- ---- -------- ------ ------
1 enet 100001 1500 - - - - - 0 0
10 enet 100010 1500 - - - - - 0 0

Switch(config)#
Switch(config)#
Switch(config)#int ran
Switch(config)#int range fast
Switch(config)#int range fastEthernet 0/1-2
Switch(config-if-range)#swi
Switch(config-if-range)#switchport mo
Switch(config-if-range)#switchport mode a
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#sw
Switch(config-if-range)#switchport a
Switch(config-if-range)#switchport access v
Switch(config-if-range)#switchport access vlan 10
Switch(config-if-range)#exit
Switch(config)#int range
Switch(config)#int range fa
Switch(config)#int range fastEthernet 0/3-4
Switch(config-if-range)#sw
Switch(config-if-range)#switchport m
Switch(config-if-range)#switchport mode a
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#w
Switch(config-if-range)#sw
Switch(config-if-range)#switchport a
Switch(config-if-range)#switchport access v
Switch(config-if-range)#switchport access vlan 20
Switch(config-if-range)#exit
Switch(config)#int range fas
Switch(config)#int range fastEthernet 0/5-6
Switch(config-if-range)#si
Switch(config-if-range)#swi
Switch(config-if-range)#switchport m
Switch(config-if-range)#switchport mode a
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#s
Switch(config-if-range)#sw
Switch(config-if-range)#switchport a
Switch(config-if-range)#switchport access vl
Switch(config-if-range)#switchport access vlan 30
Switch(config-if-range)#exit
Switch(config)#
%LINK-5-CHANGED: Interface GigabitEthernet0/1, changed state to down

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/1, changed state to down

%LINK-5-CHANGED: Interface FastEthernet0/24, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/24, changed state to up

Switch(config)#
Switch(config)#
Switch(config)#int fas
Switch(config)#int fastEthernet 0/20
Switch(config-if)#sw
Switch(config-if)#switchport m
Switch(config-if)#switchport mode t
Switch(config-if)#switchport mode trunk
Switch(config-if)#exit
Switch(config)#int fast
Switch(config)#int fastEthernet 0/24
Switch(config-if)#swi
Switch(config-if)#switchport mo
Switch(config-if)#switchport mode tru
Switch(config-if)#switchport mode trunk

Switch(config-if)#
%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/24, changed state to down

%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/24, changed state to up

Switch(config-if)#exit
Switch(config)#
%LINK-5-CHANGED: Interface FastEthernet0/20, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/20, changed state to up

vtp switch 1:
Switch#enable
Switch#config
Switch#configure ter
Switch#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#vtp
Switch(config)#vtp m
Switch(config)#vtp mode server
Device mode already VTP SERVER.
Switch(config)#vtp domain nh.com
Changing VTP domain name from NULL to nh.com
Switch(config)#'vtp password 123
^
% Invalid input detected at '^' marker.
Switch(config)#vtp password 123
Setting device VLAN database password to 123
Switch(config)#

vtp switch 2:

Switch(config)#vtp mode client
Setting device to VTP CLIENT mode.
Switch(config)#vtp password 123
Setting device VLAN database password to 123
Switch(config)#exit

setting the vlan in switch2:

Switch#enable
Switch#conf
Switch#configure ter
Switch#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Switch(config)#hostname S2
S2(config)#int fast
S2(config)#int fastEthernet 0/1-2
^
% Invalid input detected at '^' marker.
S2(config)#int range fastEthernet 0/1-2
S2(config-if-range)#swit
S2(config-if-range)#switchport m
S2(config-if-range)#switchport mode a
S2(config-if-range)#switchport mode access
S2(config-if-range)#switchport a
S2(config-if-range)#switchport access v
S2(config-if-range)#switchport access vlan 10
S2(config-if-range)#exit
S2(config)#int range fa
S2(config)#int range fastEthernet 0/3-4
S2(config-if-range)#sw
S2(config-if-range)#switchport m
S2(config-if-range)#switchport mode a
S2(config-if-range)#switchport mode access
S2(config-if-range)#sw
S2(config-if-range)#switchport a
S2(config-if-range)#switchport access vlan 20
S2(config-if-range)#exit
S2(config)#int range
S2(config)#int range fast
S2(config)#int range fastEthernet 0/5-6
S2(config-if-range)#swi
S2(config-if-range)#switchport m
S2(config-if-range)#switchport mode a
S2(config-if-range)#switchport mode access
S2(config-if-range)#swi
S2(config-if-range)#switchport a
S2(config-if-range)#switchport access v
S2(config-if-range)#switchport access vlan 30
S2(config-if-range)#
S2(config-if-range)#
S2(config-if-range)#exit
S2(config)#
S2(config)#
S2(config)#

router:
Router>enable
Router#config terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#
Router(config)#
Router(config)#
Router(config)#int gi
Router(config)#int gigabitEthernet 0/0
Router(config-if)#no shut

Router(config-if)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0, changed state to up

Router(config-if)#exit
Router(config)#int gi
Router(config)#int gigabitEthernet 0/0.10
Router(config-subif)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0.10, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0.10, changed state to up

Router(config-subif)#en
Router(config-subif)#encapsulation do
Router(config-subif)#encapsulation dot1Q 10
Router(config-subif)#ip address 192.168.0.100 255.255.255.0
Router(config-subif)#no shut'
^
% Invalid input detected at '^' marker.
Router(config-subif)#no shut
Router(config-subif)#exit
Router(config)#int gi
Router(config)#int gigabitEthernet 0/0.20
Router(config-subif)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0.20, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0.20, changed state to up

Router(config-subif)#encap
Router(config-subif)#encapsulation do
Router(config-subif)#encapsulation dot1Q 20
Router(config-subif)#ip add
Router(config-subif)#ip address 192.168.1.100 255.255.255.0
Router(config-subif)#no shut
Router(config-subif)#
Router(config-subif)#
Router(config-subif)#
Router(config-subif)#exit
Router(config)#int gi
Router(config)#int gigabitEthernet 0/0.30
Router(config-subif)#
%LINK-5-CHANGED: Interface GigabitEthernet0/0.30, changed state to up

%LINEPROTO-5-UPDOWN: Line protocol on Interface GigabitEthernet0/0.30, changed state to up

Router(config-subif)#ip add
Router(config-subif)#ip address 192.168.2.100 255.255.255.0

% Configuring IP routing on a LAN subinterface is only allowed if that
subinterface is already configured as part of an IEEE 802.10, IEEE 802.1Q,
or ISL vLAN.

Router(config-subif)#en
Router(config-subif)#encapsulation do
Router(config-subif)#encapsulation dot1Q 30
Router(config-subif)#ip address 192.168.2.100 255.255.255.0
Router(config-subif)#no shut
Router(config-subif)#
Router(config-subif)#
Router(config-subif)#exit
Router(config)#